NANO  HIGHLIGHT

Deep Subwavelength Optical Field Localization

NSF NIRT Grant 0608863

PIs: Yeshaiahu Fainman, Geert Schmid-Schoenbein, Alexander Groisman, Vitaliy Lomakin

University of California, San Diego

In 1873, Ernst Abbe discovered the fundamental resolution limit for an optical device, known as the “diffraction limit” that is typically half a wavelength. This has remained a formidable barrier for basic physics, as well as the rapidly developing on-chip miniaturization of large stationary platforms. To create a so-called lab on a chip, it is necessary to develop an approach that can overcome the “diffraction limit” and manipulate light on a deep subwavelength scale.

Deep-subwavelength optical field localization (on the order of 25 nm) by the resonant nano-focusing antenna

Yeshaiahu Fainman and colleagues at the University of California, San Diego have developed a novel plasmonic geometry that can overcome the conventional diffraction limit and strongly localize the optical field on a nanometer scale. This new structure, called a resonant nano-focusing antenna applies three different resonance and field localization mechanisms simultaneously for efficient nano-focusing and field localization: localized plasmons resonance, high effective index plasmonic edge localization, and TEM split antenna field localization.  This combination makes an ultra-high field confinement possible, while simultaneously increasing the overall efficiency of the localized fields due to the resonant nature of localized plasmons and their associated large stored near-field energy.

In an Optics Express paper [1], Dr. Fainman and colleagues reported the integration of this resonant nano-focusing antenna with on-chip Si waveguides. A gold, resonant nano-focusing antenna to be embedded inside a Si waveguide is designed and fabricated to efficiently convert the propagating waveguide mode to a localized plasmon mode, thus allowing for deep-subwavelength optical field localization in the nano capacitor-like gap of the antenna. This deep subwavelength field localization has been experimentally confirmed in their near field optical measurement with a focusing spot of about 75 nm at the telecom wavelength of 1550 nm.

This on-chip, deep subwavelength optical field localization beyond the diffraction limit is anticipated to impact multiple applications including the construction of novel on-chip optical devices for bio-medical imaging, bio-sensing, nano-lithography, heat-assisted magnetic recording, and plasmonic nanocircuits operating at optical frequencies.

References

[1] L. Feng, D. Van Orden, M. Abashin, Q. J. Wang, Y. F. Chen, V. Lomakin, and Y. Fainman,  Opt. Express 17, 4824 (2009).